## Slide 1: Introduction to Networking and TCP/IP
Lecture 2

## Slide 2: Outline
Networking Basics
Sockets
Remote Procedure Call

## Slide 3: Networking
Layering
  ISO OSI 7-layer model
    Physical, data link, network, transport, session, presentation, application
  TCP/IP model
    Physical, Link, network, transport, application

## Slide 4: TCP/IP Layering (cont.)
Network Layer
Transport Layer
Application Layer
Link Layer
ARP
IP
TCP/UDP
HTTP/FTP/SMTP
TCP/IP protocol stack
Demultiplexing
Encapsulation
Ethernet
app
app

## Slide 5: Common Protocols in TCP/IP Protocol Stack
ARP: Address Resolution Protocol
IP: Internet Protocol (RFC 791)
UDP: User Datagram Protocol (RFC 768)
TCP: Transmission Control Protocol (RFC 793)

## Slide 6: Encapsulation

## Slide 7: Protocol Headers
Ethernet header
  MAC (Ethernet) addresses
IP header
  IP addresses, protocol
TCP/UDP header
  Port numbers

## Slide 8: ARP
X
A
B
Ethernet (CSMA/CD)
Where is X?
X is here.
IP address  Ethernet address

## Slide 9: Ethernet Header

## Slide 10: IP Header

## Slide 11: UDP Header

## Slide 12: TCP Header

## Slide 13: Demultiplexing

## Slide 14: IP Addresses
IPv4 address
  Dotted decimal: 140.112.8.130
Unicast, broadcast, and multicast
Private address space
  10.0.0.0 - 10.255.255.255 (10/8 prefix)
  172.16.0.0 - 172.31.255.255 (172.16/12 prefix)
  192.168.0.0 - 192.168.255.255 (192.168/16 prefix)
Class A, B, C, D, E

## Slide 15: IP Addresses (cont.)

## Slide 16: Port Numbers
Well-known ports: 1-1023
  HTTP: 80
  SMTP: 25
  Telnet: 23
  FTP: 21 (control), 20 (data)
Others
  Gnutella: 6346, 6347
Client vs. server ports

## Slide 17: Useful Tools
Packet sniffer or analyzer
  Tcpdump
  Ethereal
  NetXRay
Packet generator
  Socket programming
Packet capture libraries
  Libpcap & WinPcap

## Slide 18: Example Scenario: Web Browsing
Client
Server
http://www.ntu.edu.tw/
80
61.2.3.4
(140.112.8.130, 80)
www.ntu.edu.tw
23
25

## Slide 19: Example Scenario: Web Browsing
Client
Server
www.ntu.edu.tw?
80
61.2.3.4
(140.112.8.130, 80)
www.ntu.edu.tw
23
25
DNS Server
140.112.8.130

## Slide 20: Example Scenario: Web Browsing
Client
connect(140.112.8.130, 80)
Server
http://www.ntu.edu.tw/
80
7890
61.2.3.4
(140.112.8.130, 80)
www.ntu.edu.tw
23
25

## Slide 21: DNS Name Resolution
X
A
DNS
Ethernet (CSMA/CD)
Where is www.ntu.edu.tw?
X is 140.112.8.130.
hostname  IP address

## Slide 22: ARP (Revisited)
X
A
B
Ethernet (CSMA/CD)
Where is 140.112.8.130?
140.112.8.130 is 00:C0:EB:00:8B:68
IP address  Ethernet address
140.112.8.130 00:C0:EB:00:8B:68

## Slide 23: Sockets
ARP: Ethernet (hardware, MAC) address
IP: IP address
TCP/UDP: port number
Port vs. service
Sockets: {IPsrc, portsrc, IPdest, portdest}

## Slide 24: Socket Connection
Client
connect(140.112.8.130, 80)
Server
(61.2.3.4, 7890)
80
7890
61.2.3.4
(140.112.8.130, 80)
www.ntu.edu.tw
23
25

## Slide 25: Socket Programming
UNIX: BSD Socket API (in C)
  socket(), bind(), listen(), accept(), connect(), send(), recv(), sendto(), recvfrom(), select(), …
Java Socket API
  java.net.Socket
Perl, Python, …

## Slide 26: Remote Procedure Call
RFC 1831 – RPC v2
RFC 1832 -- XDR: External Data Representation Standard
  A machine-independent representation of data
Local vs. remote procedure calls

## Slide 27: RPC
UDP/TCP transport
  RPC/UDP: connectionless, fast
  RPC/TCP: connection-oriented, slower
Portmap service (or portmapper)
  Port 111
  RFC 1833

## Slide 28: RPC

## Slide 29: RPC Portmapping
Client
connect(140.112.8.130, 111)
Server
111
7890
61.2.3.4
140.112.8.130
P
25
Port P
connect(140.112.8.130, P)

## Slide 30: RPC Programming
rpcgen
Applications: NFS (Network File System), …

## Slide 31: Programming Exercises
Packet sending/receiving
FTP client/server
  FTP (File Transfer Protocol): RFC 959
HTTP (Web) client/server
  HTTP (HyperText Transfer Protocol) 1.1: RFC 2616
Mail client/server
  SMTP (Simple Mail Transfer Protocol): RFC 2821
  POP3 (Post Office Protocol Version 3): RFC 1939
  IMAP4 (Internet Message Access Protocol – Verison 4rev1): RFC 3501
  MIME, …
…

## Slide 32: Further Readings
W. Richard Stallings, B. Fenner, A. M. Rudolf, UNIX Network Programming, Vol. 1: the Sockets Networking API, 3rd ed., Addison-Wesley, 2003.
E. R. Harold, Java Network Programming, 3rd ed., O’Reilly, 2004.
RFCs (Request for Comments), http://www.rfc-editor.org/